ARI

Final Report

  - Date:	September 7, 2006

  - Reporting Period:	Final

  - Project Number:	46485

  - Project Title:	Flow Rate Indexing Procedure (QIP) for Non-Standard Structures

  - Principal Investigator (s):

Dr. Stuart Styles

Irrigation Training and Research Center

BioResource and Agricultural Engr. Dept.

California Polytechnic State University, San Luis Obispo

ph: (805) 756-2429

fax: (805) 756-2433

e-mail: sstyles@calpoly.edu

Professor

  - Co-Principal Investigator (s):

Not applicable

  - Cooperator (s):

Bryce White, Water Conservation Specialist

U.S. Bureau of Reclamation, Mid-Pacific Region

2800 Cottage Way

Sacramento, CA 95825

ph: (916) 978-5208

fax: (916) 978-5290

bwhite@mp.usbr.gov

John Sloat, Senior Hydrologist

SonTek/YSI, Inc.

6837 Nancy Ridge Dr., Ste. A

San Diego, CA 92121

ph: (858) 546-8327

fax: (858) 546-8150

Traeger Cotton

SCE Agricultural Technology Application (AGTAC) Center

4175 S. Laspina St.

Tulare, CA 93724

ph: (800) 772-4822

fax: (559)625-7188

Jeff Heringer, Superintendent

Alta Irrigation District

8951 Ave. 432

Dinuba, CA 932618

ph: (559) 591-4203

fax: (559) 591-4078

jh@altaid.org

Stan Wangberg, General Manager

Anderson-Cottonwood Irrigation District

2810 Silver St.

Anderson, CA 96007

ph: (530) 365-7329

fax: (530) 365-7623

acidstan@sbcglobal.net

David Weisenberger, General Manager

Banta-Carbona Irrigation District

3514 W. Lehman Rd.

Tracy, CA 95378

ph: (209) 835-4670

fax: (209) 835-2009

bcid@inreach.com

Biggs-West Gridley Irrigation District

1713 West Biggs Gridley Rd.

Gridley, CA 95948

ph: (530) 846-3317

fax: (530) 846-5737

Jeff Quimby

Contra Costa Water District

1331 Concord Ave.

Concord, CA 94524

ph: (925) 688-8136

fax: (925) 688-8122

Mark Stuntebeck

Klamath Irrigation District

6640 Kid Lane

Klamath Falls, OR 97603

ph: (541) 882-6661

fax: (541) 882-4004

Hicham El Tal, Manager of Engineering/Water Resources

Merced Irrigation District

720 W. 20th St.

Merced, CA 95344

ph: (209) 722-5761

fax: (209) 722-6421

eltal@mercedid.org

John Sweigard, District Manager

Patterson Irrigation District

948 Orange Ave.

Patterson, CA 95363

ph: (209) 892-6233

fax: (209) 892-4013

patwater@evansinet.com

Fred Schantz, Field Manager

Sutter Mutual Water Company

PO Box 128

Robbins, CA 95676

ph: (530) 738-4423

fax: (530) 738-4327

ffschantz@aol.com

Paul Hendrix, General Manager

Tulare Irrigation District

1350 W San Joaquin Ave

Tulare, CA 93274

ph: (559) 686-3425

fax: (559) 686-3673

jph@tulareid.org

Gerald Pyle

Tulelake Irrigation District

Hwy 39 Havlina Rd

Tulelake, CA 96134

ph: (530) 667-2249

fax: (530) 667-4228

Colorado River Indian Tribes

Route 1 Box 23-B

Parker, AZ 95344

ph: (928) 916-1092

fax: (928) 669-8678

Matt Ables

Lower Colorado River Authority

3700 Lake Austin Blvd.

Austin, TX 78703

ph: (512) 473-3200

Brent Esplin/USBR Montana Area Office, for

Paradise Valley Irrigation District

2900 Fourth Avenue North

Billings, MT 59101

ph: (406) 247-7309

fax: (406) 247-7338

besplin@gp.usbr.gov

Mark Niblack/USBR Yuma Office, for

Yuma County Water Users Association

7301 Calle Agua Salada

Yuma, AZ 85364

ph: (928) 343-8253

fax: (928) 343-8320

mniblack@lc.usbr.gov

  - Prepared by:

Dr. Stuart Styles

Irrigation Training and Research Center

BioResource and Agricultural Engr. Dept.

California Polytechnic State University, San Luis Obispo

ph: 805-756-2429

fax: 805-756-2433

e-mail: sstyles@calpoly.edu

Project Director

  - Executive Summary:

Hydroacoustic flow meters are becoming standard flow measurement devices in irrigation districts throughout the western U.S.  Although hydroacoustic flow meters can be utilized in many situations where other standard flow measurement devices, such as Replogle flumes, will not work, these devices must still be properly installed and calibrated in order to give accurate flow measurement data.

Until this project, the proper installation and calibration of hydroacoustic meters at non-standard structures was not known.  As a result of this research, the calibration procedure, called Flow Rate Indexing Procedure (QIP), enables the use of hydroacoustic meters to measure and record the flow rate in a channel to within 5-10% of actual.  The research results have been successfully implemented in 7 large irrigation district projects.

The attached report details the QIP process.

  - Major Accomplishments:

    - Fine-tuning of the calibration procedure for advanced hydroacoustic flow meters, an emerging technology, resulted in the Flow Rate Indexing Procedure (QIP).  This procedure can now be used by industry and government agencies performing flow measurement.

    - The QIP process provides for greater accuracy in discharge data and stage information collection for rating non-standard sites.  The discrepancy between data collected using a hydroacoustic flow meter and calibrated using the QIP process compared to data collected using the traditional and much more expensive Replogle flume was reduced dramatically as a result of this study.

    - The ability to use hydroacoustic meters was demonstrated at 16 irrigation districts.  The successful implementation of the QIP will significantly help with the accuracy of evaluating the flow rate at the sites evaluated.

  - Impact Statements:

    - This project is enabling irrigation districts to significantly expand their modernization and water conservation efforts through better water measurement.

    - USBR hydrologists and irrigation district personnel are using the QIP process to index sites throughout Sacramento, Klamath, Yuma, and Fallon areas.

    - As a result of their participation in this project manufacturers of hydroacoustic flow meters have modified and upgraded their equipment and software to incorporate the capability for new data collection features.  The new data collected has been incorporated into the final project technical report.

  - Dissemination, publications and presentations of research:

The final report is a 262 page document that includes extensive data and details on the correct procedures for evaluating a flow measurement site.  The report will be made available to the cooperating districts and agencies as well as being posted to the ITRC web site.

ITRC Web Site:

The ITRC web site is widely used by irrigation districts and consultants as a source of information.

a.	Canal Flow Rate Measurement Guidelines - ITRC 2005: Hydroacoustic Meters (R 05-002):  http://www.itrc.org/reports/sensors/hydroacousticsummary.htm

Professional Articles:

The following all contain information developed in this research:

a.	Styles, S.W. and M. Niblack.  2003.  Canal Velocity Indexing at Colorado River Indian Tribes (CRIT) Irrigation Project in Parker, Arizona using the SonTek Argonaut SL.  Proceedings of the Annual Technical Conference of the Irrigation Association.  November 18-20.  San Diego, CA. (published conference proceedings)

b.	USCID March 2004 - Workshop on Application of Technology to Water Measurement and Management

Procedure and User Instructions

a.	Procedure for using Acoustic Doppler Current Profilers (ADCPs)

b.	User Instructions for Regression Analysis of Hydrological Data using Excel

Training and Demonstration

      - USBR hydrologists and district staff were directly trained by ITRC during the course of the study

      - ITRC performs 3-4 flow measurement classes per year.  Material generated by this report will be disseminated into those courses.