Standard Operating Procedure: LECO MSX-250A

| 1. Place the work onto the table and lock in place by pushing the clamp up against the work and push the rods down to secure the work. |  |
| --- | --- |

| 2. Adjust the sprayers so that they shoot water onto the tip of the blade, but far up enough that water still hits the blade while the blade wears down during cutting. |  |
| --- | --- |

| 3. WHILE THE MACHINE IS OFF, leave the safe guard up and bring the blade down as if making the cut to scout clearance of the sprayers and blade and adjust accordingly. |  |
| --- | --- |

| 4. Lower the safe guard and turn the main power switch to the ¦ position. |  |
| --- | --- |

| 5. Push the CONTROL ON button. |  |
| --- | --- |

# Text boxes

Rods

Table